## Slide 1
Atomic Icebreaking Fleet =
Development of the Northern Sea Route
ROSATOMFLOT
Image by NASA
“Russia faces Arctic Ocean and no other nation needs icebreakers so much as we do. The nature shackled us in ice and the faster we drop these shackles, the sooner we let Russian power to unfold”.
Vice-Admiral Stepan Makarov

## Slide 2: Northern Sea Route
Draught 12,5 m
Draught 18 m
Murmansk
Vitino
c Drovyanoy, Yamal
We need to develop the best economic model for the Northern Sea Route, so that by 2015 we raise its cargo tonnage up to 4 million tons a year. We have to speed up the construction of ice-class vessels and of new nuclear- and diesel-powered icebreakers (plans have been developed; we should carefully control their implementation). We also need to complete the creation of a modern navigation, communication, technical maintenance and emergency relief infrastructure along the entire length of the Northern Sea Route.
From the speech by Russian Federation President Vladimir Putin at the meeting of the Security Council on state policy in the Arctic, April 22, 2014

## Slide 3: Northern Sea Route is the highway to European and Asian markets
Oil and Gas from Murmansk |  |  |  |  | 
State | through Suez Canal |  | through NSR |  | +/- days
Japan (p. Kobe) | 12291 miles | 37,1 days | 6010 miles | 18,1 days | -19
Korea (p. Busan) | 12266 miles | 37 days | 6097 miles | 18,4 days | -18,6
China (p. Ningbo) | 11848 miles | 35,8 days | 6577 miles | 19,9 days | -15,9
From Rotterdam to the Asian markets |  |  |  |  | 
State | through Suez Canal |  | through NSR |  | +/- days
Japan (p. Kobe) | 10969 miles | 33,1 days | 7610 miles | 23 days | - 10,1
Korea (p. Busan) | 10754 miles | 32,5 days | 7697 miles | 23,2 days | - 9,3
China (p. Ningbo) | 10336 miles | 31,2 days | 8177 miles | 24,7 days | - 6,5
c. Drovyanoy, Yamal
Northern Sea Route
Vitino
Suez Canal
China
p. Ningbo
Korea
p. Busan
Japan
p. Kobe
Murmansk
Rotterdam

## Slide 4
The Late Transit via NSR by
Tor Viking II piloted by ib Rossiya
December 16-25, 2010
The Early Transit via NSR by
mv Kapitan Myshevskiy piloted by ib Sibir
May 28 – June 13, 1978
The voyage by Swedish supply icebreaker Tor Viking II piloted by atomic icebreaker Rossiya was done a month after the official completion of summer-to-autumn navigation on the NSR. This successful transit voyage done in late December in 9 days proved that it is possible to increase the period of Arctic navigation on the NSR in winter months.
Mv Kapitan Myshevskiy left port of Murmansk on May 26, 1978 with cargo for Polar Station – 24. On May 28 she was taken under pilotage by atomic ib Sibir near Novaya Zemlya and brought to Bering Strait on June 13. Kapitan Myshevskiy called on port of Magadan on June 22, 1978.

## Slide 5
Mv Nordic Orion carrying 66 000 t of Iron Ore from Murmansk, Russia
to Lanshan, China via the NSR
July 07, 2013

## Slide 6
Mt Propontis
Deadweight : 117 055 t
Cargo: naphtha 79 846 t
Loading Port: Mongstad, Norway
Destination Port: Mizushima, Japan
NSR period: 24.07-05.08.13
Cargo: gasoil 109 090 t
Loading Port: Ulsan, Korea
Destination Port: Skaw, Denmark
NSR period: 25.09-06.10.13

## Slide 7: LNG Transit via the Northern Sea Route
LNG Ob River
Ice Class: 1A (Arc 4)
Cargo capacity: 149 755 m3
Ballast:
Westbound 08-16.10.2012
Cargo:
Eastbound 09-18.11.2012
LNG Arctic Aurora
Ice Class: 1A (Arc 4)
Cargo capacity: 150 000 m3
Ballast:
Westbound 06-18.08.2013
Cargo:
Eastbound 22.09-06.10.2013

## Slide 8
NSR Caravan Piloting
July 2012
Mv Nordic Odyssey, ttb Vengeri, mt Marilee, mv Kapitan Danilkin
ice-piloted by ib Yamal and Vaygach July 12 – 22, 2012

## Slide 9
Pilot Voyages 2013
Mv Yong Sheng:
NSR period: 26.08 – 03.09.2013
(7,5 days)
Deadweight:16651 tons
Cargo: general cargo & equipment
Owner: COSCO Shipping
Mt Stena Polaris:
NSR period: 28.09 – 11.10.2013
Deadweight: 75 000 tons
Cargo: naphtha from Ust-Luga
Owner: Stena Shipping
Sponsored: Ministry of Ocean & Fisheries of the Republic of Korea
Charterer: Hyundai Glovis Co

## Slide 10: Total of Transit Voyages in 2010-2013
 | 2010 | 2011 | 2012 | 2013
Total Volume of Transit Cargo, t | 111 000 | 820 789 | 1 261 545 | 1 355 897
Total Number of Transit Voyages | 4 (2 of them in ballast) | 34 (10 of them in ballast) | 46 (13 of them in ballast) | 71 (22 of them in ballast)
NSR Transit 2013 Cargo
Cargo Type | Number of Vessels | Volume, t | Displacement, t | Cargo Volume Eastbound, t | Cargo Volume Westbound, t
Liquid | 31 | 911 867 |  | 588 659 | 323 208
Bulk | 4 | 276 939 |  | 203 439 | 73 500
LNG | 1 | 66 868 |  | 66 868 | 
General | 13 | 100 223 |  | 36 846 | 63 377
Ballast | 15 |  | 469 703 |  | 
Repositioning | 7 |  | 38 027 |  | 
Total: | 71 | 1 355 897 | 507 730 | 895 812 | 460 085

## Slide 11
Icebreaking pilotage of Northern Navy Fleet ships headed by heavy atomic missile cruiser Petr Velikiy
September 08-10, 2013 through Vilkitskiy Strait eastbound
Ships have NO ice class

## Slide 12: Atomic icebreaker 50 Let Pobedy delivered Olympic Flame to the North Pole on October 19, 2013

## Slide 13: What’s next?

## Slide 14
I. Cargo base for the Northern Sea Route
Hammerfest
Narvik
Oulu
Primorsk,
Ust-Luga
Murmansk
p. Vitino
p. Sabetta
Hokkaido
Kobe
Busan
Qingdao
Prince Rupert
Vancouver
Beaufort Sea
Petropavlovsk-Kamchatsky
West-East | East-West
LNG(p. Sabetta, Hammerfest) Iron Ore (Murmansk, Narvik) Crude Oil (Primorsk) Gas condensate (Ust-Luga, p. Vitino) | Coal (Prince Rupert, Vancouver) Fish (Petropavlovsk-Kamchatsky, Hokkaido) Light oil products (Busan, Inchon) Seasonal container cargoes (Busan, Hokkaido)
Total: 15 mln. transit tons per year + 17,6 mln. LNG from p. Sabetta + 10 mln. tons of oil from Noviy Port | 
Inchon
Transit 15 mln. tons
LNG from Yamal p-la 17,6 mln. tons
10 mln. tons of oil

## Slide 15
Sea Canal
Sabetta Port
Approach Canal
Key transport components:
A fleet of 16 arctic LNG-tankers;
Sea port in the area of Sabetta town;
Port fleet consisting of 5 vessels of different type;;
Support of atomic icebreaking fleet;
Navigation safety system.
LNG & Gas Condensate export, thousands tons |  |  |  |  |  | 
2017 | 2018 | 2019 | 2020 | 2021-2038 | 2039 | 2040
800 | 6 100 | 11 900 | 16 700 | 17 600 | 17 400 | 16800
Yamal LNG

## Slide 16
Novy Port Oil Field is the largest on the Yamal Peninsula by the volume
of oil and gas condensate
Novy Port Oil Field
Cape Kamenniy
Novy Port
Is the basic project of JSC Gazprom Neft on the Yamal Peninsula ;
Located in Yamal-Nenets Autonomous District Region within 30 km of Obskaya bay coast and 250 km of town of Nadym;
Extractable resources constitute 222 mln tons of oil, 211 billion m3 of gas, 17mln tons of condensate;
Project is unique due to year-round export of oil by sea in harsh climatic conditions.
2015 | 2016 | 2017- 2027 | 2028 | 2029 | 2030
600 | 3 000 | 5 000 | 4 000 | 3 000 | 2 500
Extraction of Oil at Novy Port Field,
mln tons

## Slide 17
c.
JSC Payakha is a part of JSC Independent Oil and Gas Company group and is 100% its subsidiary.
JSC Payakha holds 2 licenses for geological study, search, field works and extraction of hydrocarbons on Payakhskiy (till 2024) and North-Payakhskiy (till 2035) areas of subsoil in Taimyrskiy Dolgano-Nenetskiy distcrict of Krasnoyarskiy Region.
The Fields are located in Eastern Siberia to the north of polar Circle (400 km), within 140 km north of Dudinka town which is a river and sea port supporting year-round navigation through the Northern Sea Route.
Within 50 km north of the field on the banks of Yenisei river (cape Tanalau) there will be built an oil loading terminal (2300 km from port of Murmansk and 5400 km from port of Rotterdam) and preliminary cargo storage terminal to serve the fields. From there cargoes will be transported by trucks.
 | 2015 | 2016 | 2017 | 2018 - 2028 | 2029 | 2030
Oil Extraction, thousand tons | 6 | 360 | 1388 | 3 000 | 1916 | 1809
Export of JSC Payakha products

## Slide 18
Export of Norilsk Nickel products
the world’s largest producer of nickel and palladium
one of the world’s leading producers of platinum and copper.
The Company produces cobalt, rhodium, silver, gold, iridium, ruthenium, selenium, tellurium and sulfur.
The Polar Division is located above the Polar Circle on the Taimyr Peninsula (Krasnoyarsky Region). Its entities are connected to suppliers and buyers via the Yenisei river and the Northern Sea Route, as well as by air.
Main port of export for finished product and delivery of supplies is the port of Dudinka located in the low reaches of Yenisei. Nautical navigation in the port is done year-round (provided by atomic icebreaking fleet in winter-to-autumn period).
FSUE Atomflot and Norilsk Nikel have signed a 3-year contract for icebreaking support. In 2014 another 3-year contact for the period 2015-2017 is planned to be signed.
Annual total volume of finished product and supplies transhipped through port of Dudinka is 1,3 mln tonn.

## Slide 19
II. Ice Conditions in the Russian Arctic
Satellite Image of Ice Conditions in the Russian sector of Arctic dd. 17.09.2013
Ice Concentration 1-6
Ice Concentration 7-10
17-18.09.2012
40% ice area increase compared to 2012

## Slide 20
Ice Conditions by Periods:
 | Ice Concentration 1-6 points |  | Ice Concentration 7-10 points
 | Extra Young Ice |  | Fast Ice
 | Young Ice (0-30 cm) |  | Clear
 | One-Year Ice (30-200 cm) |  | 
 | Ice Area Border according to TV/IR/microwave |  | 
28-30.07.13
07-09.07.13
11-13.08.13
15-17.09.13
06-08.10.13
10-12.11.13

## Slide 21
III. Atomic Icebreaking Fleet
and Further Development

## Slide 22
Federal State Unitary Enterprise of Atomic Fleet
Atomic Fleet has 18 units:
Personnel: 1158
  Atomic Vessels - 10
      Atomic Icebreakers – 9
      Among them operational - 5
      Atomic container carrier - 1
    Special Vessels – 5
    Floating Port Crane
    2 Floating Docks
      Coastal Facilities:
      Personnel: 856
      base for the atomic icebreaking fleet;
      full complex of ship repair;
      nuclear fuel handling;
      radioactive wastes handling.

## Slide 23
Atomic Icebreaking Fleet
Atomic icebreakers of “Arktika” type:
Propulsion Capacity – 54 MW Water displacement – 23000 t
Draught – 11,0 m
Icebreaking capability – 2,25 m
i/b “Sovetsky Soyuz” – 29.12.1989 i/b “Yamal” – 28.10.1992 i/b “50 Let Pobedy” – 23.03.2007
Atomic Icebreakers of “Taimyr” type:
Propulsion capacity – 35 MW Water displacement 21000 t
Draught – 8,1 m
Icebreaking Capability – 1,7 m
i/b “Taimyr” – 30.06.1989
i/b “Yaygach” – 25.07.1990
Universal Atomic Icebreaker Project 22220 (IB60)
Propulsion Capacity– 60 MW Water displacement 33530 / 25 540 t
Draught – 10,5 / 8,5 m
Icebreaking capability – 2,9 м
1st IB60 – 31.12.2017
2nd IB60 – year 2019
3rd IB60 – year 2020

## Slide 24
Med-term Operational Period of Atomic Icebreakers
(with Nuclear Power Plant resource of 150-200 000 hours)
- Linear icebreakers operational period
- Low-draught icebreakers operational period
- New universal icebreakers operational period
Наименование | Год ввода в эксплуатацию | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027
Тaimyr | 1989 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Vaygach | 1990 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Rossiya | 1985 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sovetskiy Soyuz | 1989 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Yamal | 1992 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
50 Let Pobedy | 2007 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commission of Universal Atomic Icebreakers (IB-60 type) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1st IB-60 | 2017 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2nd IB-60 | 2019 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3rd IB-60 | 2020 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
- If prolonged up to 175 000 hours
- If prolonged up to 175 000 hours
- If prolonged up to 200 000 hours
Notes: ,kextybz gthcjfykf

## Slide 25
Chart: Icebreakers per month
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Обская губа (Ямал СПГ+Газпром нефть) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 1 | 1 | 3 | 7 | 7 | 7 | 8 | 21.5 | 23 | 23 | 23
#REF! | 1
Енисей (Нор.Никель + ННК) | 26 | 26 | 26 | 26 | 26 | 26 | 25 | 21 | 14 | 5 | 0 | 5 | 5 | 5 | 5 | 5 | 5 | 7 | 7 | 7 | 7 | 7
Транзиты в акватории СМП | 0 | 5 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 10 | 10 | 10 | 10
Экспедиции | 0 | 3 | 7 | 5 | 2 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4
#REF! | 1
Круизы | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 0
#REF! | 1
Белое море | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 | 0
Балтийское море | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 0
Итого за год | 32 | 32 | 32 | 32 | 32 | 32 | 31 | 27 | 21 | 14 | 18 | 25 | 22 | 25 | 27 | 25 | 25 | 29 | 42.5 | 44 | 44 | 44
Conclusions:
With the development of major projects in the Russian sector of Arctic, growing interest of international shipping community to NSR transit navigation, new tasks set before Russian Navy and positive dynamics of ice area increase, the demand for powerful and autonomous icebreakers with nuclear power plants will keep growing.
Considering the schedule of icebreakers decommissioning due to end of nuclear power plant lifespan it is vital to complete construction of universal atomic icebreakers not later than:
1st IB60 – 31.12.2017 (contractual date)
2nd IB60 – before end of 2019 – beginning of 2020 year
3rd IB60 – before end of 2020 – beginning of 2021 year
Rosatomflot basic clients for the period 2000-2021

## Slide 26
Thank you for your attention!